The CLI Module
Synopsis
This is a (budding) set of tools to help with writing command line and others scripts.
# Loading the tools.
This is done with the standard import and load statement like
   module_import(module_load(info().lib.cli, 'java'))
cli
## The to_stem function
This will take a set of arguments (probably from the command line, but you can pass it whatever list you like) and it will process them into a usable stem. This means separating out the switches and flags and organizing the other arguments in order.
### Definitions
switch - an argument to the program prefixed with a marker. The immediate successor to it is its value. (e.g. -format iso8601)
flag - an argument which has no value, but is either present or not (e.g. -verbose).
Function arguments are
arg. - the list of command line arguments. If omitted this defaults to the contents of the arg() function
marker - a string that starts a flag or switch
flags. - list of flags
Examples
Let us say that we had a script that was invoked with the following:
   do_it.qdl my_key.pem -user bob -version 1.2 -v -format iso8601 -in input.txt output.txt

if you issue the args() command you will see the arguments are
   args()
[my_key.pem, -user, bob, -version, 1.2, -v, -format, iso8601, -in, input.txt, output.txt]

There is a flag (-v) and what if there is a flag like -use_ssl that, when missing indicates the default is false? Here is what you could do
   r. := to_stem(args(), ['-v','-use_ssl'])
   r.
[my_key.pem,output.txt]~{
 -use_ssl : false,
 -version : 1.2,
      -in : input.txt,
    -user : bob,
       -v : true,
  -format : iso8601
}

Note that access to these values is quite easy. To get the last argument issue
r.(-1)

To check if the user wants to use ssl:
if[r.'-use_ssl'][…]

To check if the user passed in a specific switch:
if[has_key('-format', r.)][…];

You can even specify special switches
to_stem(args(), '-', ['--help','--version']

which tells the system to look for those flags first so you can test them for, e.g., printing help or version information.